## Slide 1: Content
1) Analysis with single source
Methodology [Section 10.1]
Two examples
2) Analysis with multiple sources (single frequency)
Nodal analysis [Section 10.2] (1 example)
Mesh analysis [Section 10.3] (1 example)
3) Analysis by superposition (multiple frequencies)
Circuits containing DC sources and AC sources of a single frequency (1 example)
Circuits containing multiple AC sources with different frequencies (1 example)
4) AC Power: Instantaneous vs. Average
Alexander & Sadiku,
“Fundamentals of Electric Circuits”
7th Edition Chapters 9 &10

## Slide 2: General methodology
Transform the circuit to the frequency domain
Transform AC sources from time domain sinusoids to phasor form
Work out impedances for a given frequency ω
Solve the problem using circuit techniques
Transform phasor form solutions back to time domain
(Time-domain representation)
(Phasor-domain representation)

## Slide 3: 1A) Single source analysis example 1
Alexander 9.50
Given that
Step 1a: Transform source to phasor
Step 1b: Work out the impedance values
1 mF  -j/(100*0.001) = -j10
0.1 H  j100*0.1 = j10
Step 2: Solve using circuit analysis methods
Using current divider rule,
Step 3: Transform back to time domain
j10
-j10
Ix

## Slide 4: 1B) Single source analysis example 2
Alexander 9.42
Determine vo(t)
Step 1a: Transform source to phasor
Step 1b: Work out the impedance values
50 µF  -j/(200*50*10-6) = -j100
0.1 H  j200*0.1 = j20
Step 2: Solve using circuit analysis methods
Using voltage divider role,
Step 3: Transform back to time domain
-j100
j20

## Slide 5: 2A) Single freq multiple sources example 1
Focus only on STEP 2 (solving by circuit techniques) in this example
Alexander 10.16
Use MESH CURRENT ANALYSIS to find Vx
Applying KVL around mesh Ix:
Ix*(j4 - j3 + 5) – (2)*(5) + (3*(-j3) = 0
Ix = 1.43748.94o A
Vx = (1.43748.94o )*(j4) = 5.749138.94o V
Ix

## Slide 6: 2B) Single freq multiple sources example 2
Alexander 10.26
Use nodal voltage analysis to find io(t)
Step 1a: Transform source to phasor
10  100o, ω = 103 rad/s
20  20-90o, ω = 103 rad/s
Step 1b: Work out the impedance values
1 µF  -j/(103*10-6) = -j1000
0.4 H  j103*0.4 = j400
Step 2: Solve using circuit analysis methods
Applying KCL at node Vo:
Vo = 15.871.57o V
Io = (15.871.57o)/j400 = 39.5-18.43o mA
Step 3: Transform back to time domain
Io = 39.5-18.43o mA, ω = 103 rad/s  io(t) = 39.5 cos(103t – 18.43o) mA
100o
-j1000
j400
20-90o
Vo

## Slide 7: 3A) Superposition (multiple freq) example 1
Alexander 10.44 (Modified)
Given vs(t) = 50cos(2t) and is = 0.9 A, find vx(t)
Method: Analyze circuit one frequency at a time
In the case, first analyze at DC then at 2 rad/s and then add up the two solutions (superposition)
At DC, redraw circuit without vs(t):
Replace voltage source with short circuit
Replace inductor with short circuit
Resistance across current source = 20 16 = 80/9 Ω
Vx = 0.9*80/9 = 8 V (DC)

## Slide 8: 3A) Superposition (multiple freq) example 1
Alexander 10.44 (Modified)
Given vs(t) = 50cos(2t) and is = 0.9 A, find vx(t)
At 2 rad/s, redraw circuit without is:
Replace current source with open circuit
Step 1a: Transform source to phasor
50cos(2t)  500o, ω = 2 rad/s
Step 1b: Work out the impedance values
5 H  j2*5 = j10
Step 2: Solve using circuit analysis methods
Using voltage divider rule,
Vx = (500o) = 21.41-15.52o
Step 3: Transform back to time domain
Vx = 21.41-15.52o, ω = 2 rad/s
 vx(t) = 21.41cos(2t – 15.52o) V
(NEVER SKIP THIS STEP)
Note that there are 2 terms in the final form (one at DC and another at 2 rad/s)
j10
500o
Final step: Add up both solutions
vx(t) = 21.41cos(2t – 15.52o) + 8 V

## Slide 9: 3B) Superposition (multiple freq) example 2
Alexander 10.45
Find i(t)
At 4 rad/s, redraw circuit without 10 rad/s source:
Replace 10 rad/s voltage source with short circuit
Step 2: Solve using circuit analysis methods
I*(20 + j1.2) + 6-90o = 0
I = 0.299586.57o A
Step 3: Transform back to time domain
I = 0.299586.57o , ω = 4 rad/s
 i(t) = 0.2995 cos(4t + 86.57o) A
NEVER SKIP THIS STEP
Method: Analyze circuit one frequency at a time
In the case, first analyze at 4 rad/s then 10 rad/s.
Finally, add up the two solutions (superposition)
Step 1a: Transform source to phasor
6sin(4t)  6-90o, ω = 4 rad/s
Step 1b: Work out the impedance values
300 mH  j4*0.3 = j1.2

## Slide 10: 3B) Superposition (multiple freq) example 2
Alexander 10.45
Find i(t)
At 10 rad/s, redraw circuit without 4 rad/s source:
Replace 4 rad/s voltage source with short circuit
Step 2: Solve using circuit analysis methods
I*(20 + j3) = 1630o
I = 0.791121.47o A
Step 3: Transform back to time domain
I = 0.791121.47o , ω = 10 rad/s
 i(t) = 0.7911 cos(10t + 21.47o) A
Step 1a: Transform source to phasor
16 cos(10t + 30o)  1630o, ω = 10 rad/s
Step 1b: Work out the impedance values
300 mH  j10*0.3 = j3
NEVER SKIP THIS STEP
Final step: Add up both solutions
i(t) = 0.2995 cos(4t + 86.57o) + 0.7911 cos(10t + 21.47o) A
Note that there are 2 terms in the final form (one at 4 rad/s and another at 10 rad/s)
1630o
j3

## Slide 11: AC Power: Instantaneous vs. Average
Mean of V = 0
Mean of V2 = 12.5 (DC offset)
V(t) = 5cos(2πt) V
V2(t) = 52cos2(2πt) V
Although the average voltage across a resistor with a sinusoidal AC voltage across it is zero, note that the average power dissipated is not zero. Since P = V2/R, we should consider the square of the voltage.
The following graph shows the voltage across a 1Ω resistor in blue and the corresponding square of this voltage in red. The red curve therefore shows the INSTANTANEOUS POWER.
The instantaneous power is clearly sinusoidal with a DC offset:
V2(t) = 52 * 0.5 * (1 + cos(4πt))
= Vpeak2 * 0.5 * cos(4πt) +
Vpeak2 * 0.5
= 12.5cos(4πt) + 12.5
Average power of V2(t) is 12.5 W
Average power of V2(t) = 0.5 * Vpeak2

## Slide 12: Effective or RMS Value
The average power absorbed by the resistor in the ac circuit of Fig. (a) is
To find the dc effective current Ieff (Fig. (b)) that will transfer the same power to resistor R as the sinusoid i(t):
Equating these two expressions of P and solving for Ieff, we obtain

## Slide 13: Effective or RMS Value
The effective value of the voltage is found in the same way as current, i.e.,
This indicates that the effective value is the square root of the mean (or average) of the square of the periodic signal. Therefore, the effective value is known as the root-mean-square (rms) value. We write
For the sinusoid i(t) = Im cos ωt, the effective or rms value is
=

## Slide 14: Effective or RMS Value
Similarly, for v(t) = Vm cos ωt:
Note: The simple formulas for Vrms and Irms are only valid for sinusoidal signals.
The average power absorbed by the resistor R in the previous simple circuit (Fig.(a) and (b)) can be written as